 Example 4
Sodaq, SPS30 and DS18X20

# 1. Foreword

April 2020
First tests to sent SPS30 and BM18x20 results to AllThingsTalk. The SPS30 library I have developed already a year ago and is used in many situations. This is the first time connect with SODAQ board of NB-IoT connection with Vodafone.

September 2020
Now added support for T-Mobile as well as sending the data in either Jason, ABCL or CBOR data format.

Paul van Haastrecht
paulvha@hotmail.com

# 2. Solution
## 2.1 Hardware
### 2.1.1 Serial connection

  SPS30 pin SODAQ
  1 VCC -------- 5V
  2 RX ---------- 1 TX
  3 TX ---------- 0 RX
  4 Select------- NOT CONNECTED (Select Serial)
  5 GND ------- GND

The DS18x20 sensor :
        DS18x20 SODAQ
    ------ GND ------------- GND
  |-| 4k7 |-- VCC /red --------- 3V3
  | ------
  |----------- data/yellow ------- D4

 You MUST connect a resistor of at least 4K7 between data and VCC for pull-up.
### 2.1.2 I2C connection
The connection for the SPS30 is with I2C. The SODAQ AFF/SARA has 2 I2C channels; SDA/SCL and SDA1/SCL1. When connecting as indicated below to SDA and SCL those pull-up resistors are already on the SODAQ board. This is the only connection that is supported by the driver.

 SPS30 pin SODAQ
  1 VCC --------------- 5V
  2 SDA --------------- SDA (next to ARF NOT A4 / SDA1)
  3 SCL ---------------- SCL (next to SDA/ARF NOT A5/ SCL1)
  4 Select -------------- GND (select I2c)
  5 GND --------------- GND

The DS18x20 sensor :
        DS18x20 SODAQ
    ------ GND ------------- GND
  |-| 4k7 |-- VCC /red --------- 3V3
  | ------
  |----------- data/yellow ------- D4

 You MUST connect a resistor of at least 4K7 between data and VCC for pull-up.

## 2.2 Software
Apart from this sketch the following libraries are necessary :

The following SODAQ drivers :
https://github.com/SodaqMoja/Sodaq_R4X
https://github.com/SodaqMoja/Sodaq_wdt

The latest SPS30 driver version 1.3.10: https://github.com/paulvha/sps30
For detailed description of setup and configuration see the SPS30.odt on the github

The latest versions of :
The DS18x20 sensor https://github.com/PaulStoffregen/OneWire

The solution has been tested on IDE version 1.8.12 & 1.8.13

If CBOR is required (see 3.1). This is available from the Arduino library manager so I recommend using that or you can download https://github.com/telecombretagne/YACL
# 3 Configure Sketch
## 3.1 Enable CBOR data format
Concise Binary Object Representation (CBOR) is a standardized data format that allows shorter message which are translated on the server to Jason. To enable remove the comments before :
//#define INCLUDE_CBOR 1
## 3.2 Select SPS30 connection
Around line 125 select either SPS30 serial (chapter 2.1.1) OR i2c (chapter 2.1.2)
#define SP30_COMMS SERIALPORT
I2C -> I2C_COMMS
serial -> SERIALPORT
## 3.3 Select the size of the SPS30 ID
By default the last 4 digits are taken from the SPS30 serial number to form the unique sensor-id that is transmitted as part of the payload. You can change that up to the maximum size of serial number.
#define SPSID 4
## 3.4 Select provider & information
You need to select the provider and connection information. Remove the comments, as done for T-Mobile :

// NL VODAFONE NB-IoT
/*
 const char* provider = "NL VODAFONE NB-IoT";
 const char* apn = "nb.inetd.gdsp";
 const char* forceOperator = "20404"; // optional - depends on SIM / network
 const char* urat = "8";
 const char* API_ENDPOINT = "api.allthingstalk.io";
 const uint16_t API_PORT = 8891;

Select_Operator Operator = S_VODAFONE; // use Jason format
//Select_Operator Operator = S_VODAFONE_A; // use ABCL format
//Select_Operator Operator = S_VODAFONE_C; // use CBOR format
*/
// NL VODAFONE LTE-M (not tested)
/*
const char* provider = "NL VODAFONE LTE-M";
const char* apn = "live.vodafone.com";
const char* forceOperator = "20404"; // optional - depends on SIM / network
const char* urat = "7";
const uint16_t API_PORT = 8891;

Select_Operator Operator = S_VODAFONE; // use Jason format
//Select_Operator Operator = S_VODAFONE_A; // use ABCL format
//Select_Operator Operator = S_VODAFONE_C; // use CBOR format
*/

// NL KPN (not tested)
/*
const char* provider = "NL KPN";
const char* apn = "internet.m2m";
const char* forceOperator = "20408"; // optional - depends on SIM / network
const uint16_t API_PORT = 8891;
Select_Operator Operator = S_KPN;
Select_Operator Operator = S_KPN; // use Jason format
//Select_Operator Operator = S_KPN_A; // use ABCL format
// Select_Operator Operator = S_KPN_C; // use CBOR format
*/

// NL T-Mobile
// * <<<<< HERE EXTRA COMMENTS
 const char* provider = "NL T-MOBILE NB-IoT";
 const char* apn = "cdp.iot.t-mobile.nl";
 const char* forceOperator = "20416"; // optional - depends on SIM / network
 const char* urat = "8";
 const char* API_ENDPOINT = "172.27.131.100";
 const uint16_t API_PORT = 15683;

Select_Operator Operator = S_TMOBILE; // use Jason format
//Select_Operator Operator = S_TMOBILE_A; // use ABCL format
// Select_Operator Operator = S_TMOBILE_C; // use CBOR format
// */ <<<<< HERE EXTRA COMMENTS

NOTE1: you need to select ONE operator. Depending the selection the data is either formatted in Jason, ABCL or CBOR.

## 3.5 Debug information
Optionally you can get debug information :
#define SPS30_DEBUG 0
A 1 (ONE) will show sending receiving data between board and SPS30. Setting as 2 (TWO) you can also get protocol errors. (if any)

#define SODAQ_DEBUG 0
A 1 (ONE) will show sending receiving data. You need to define “DEBUG” in top of , around line 36 (#define DEBUG ) in Sodaq_R4X.cpp

#define SKETCH_DEBUG 0
A 1 (ONE) will show debug data from the sketch.

## 3.6 Measurement interval

#define MEASUREMENTPERIOD 60000
time between sending update to AllTHingSTalk (ms) (60000 = 60 sec)

#define MEASUREINTERVAL 5000
delay between measurement in mS (5000 = 5 seconds)

## 3.7 DS18x20 constants

#define TEMP_PIN 4
To which pin is the data wire of the DS18x20 connected (D4)

#define TEMP_TYPE 0
 Define reading in Fahrenheit or Celsius
 1 = Celsius,	0 = Fahrenheit
## 3.8 Authentication
After you opened the Example2 in the Arduino IDE, you will a second tab “ keys.h”. In order to
access you device on AllThingsTalk, you will need to copy the authentication information here :

char* DEVICE_ID = "yourdeviceid";
char* DEVICE_TOKEN = "yourdevicetoken";

See chapter 4.5 where to obtain this information.

This is NOT necessary when using T-Mobile!!

# 4. configure AllThingsTalk
## 4.1 login

https://vodafone.allthingstalk.com

Sign in or sign up.

NOTE : This is a DIFFERENT URL than for T-Mobile. Completely different environment and as such the login credentials and password are unique for this environment (and thus different to T-Mobile)
## 4.2 Create a new ground

The back-end is organized in so-called “grounds”. A ground is a group of devices. For this
document I will call it “sps30”. Then double click on “sps30” and you will see the following:

## 4.3. Create a new device

Click on “+NEW DEVICE”, and you will get something like. >>>>>>>>>>>>>>>>>>>>>>>

I select “your own NB-IoT device” and you can select Vodafone: vvvvvvvvv

The following information is requested :

Enter a name >>>
( e.g. SPS30+DS18)

Printed on the card >>>

Optional >>>>

Optional >>>

Last press >>>>>>>>>

IMEI can be obtained from the sim card : AT+CGSN (already printed on the card)
IMSI can be obtained from the sim card : AT+CIMI
SIM can be obtained from the sim card : AT+CCID (already printed on the card)

## 4.4. Create assets

Now create new asset, press “+NEW ASSET”

For Example4 you need to add the following information:

name Choose type	CREATE ASSET
ID	String	x
M1	Number	x
M2	Number	x
M10	Number	x
TEMP	Number	x

- Each asset needs to be created separate.
- Use capitals for the name as shown.
- If you change or add in the Example4, make sure to change/add here as well.

## 4.5 Authentication

If you are done with creating assets as defined in 4.4, the DEVICE will all it’s assets like :

Now we need to get the authorization information, select
“ * SETTINGS ” top right in the screen:

The drop down menu will appear , now select ” Authentication”

>>>>>>>>>>>>>>>>>>
>>>>>>>>>>>>>>>>>>
>>>>>>>>>>>>>>>>>>

The following screen will appear :

Copy Device ID

Click on the 2 blue sheets before “Zg0..”
and paste in keys.h, part off the Example directory.
>>>>>>>>>>>>>>

Copy the Device Tokens. Click on the 2 blue sheets before “Vodafone” and paste in keys.h, part off the Example directory.

>>>>>>>>>>>>>>

If NO token >>>>>>>

See chapter 3.8 for the correct location in keys.h.

## 4.6 Jason or CBOR data format
You are done !

If you finished press DEBUG to see the packages coming in, once the board starts sending

Jason will look like:

Binary Conversion	2020-09-06T12:50:02	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 2.86}, "M2": {"value": 3.02}, "M10": {"value": 3.02}, "TEMP": {"value": 20.31}} using JSON

CBOR will look like:

Binary Conversion	2020-09-06T12:57:23	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 4.284894943237305}, "M2": {"value": 4.525962829589844}, "M10": {"value": 4.525962829589844}, "TEMP": {"value": 20.375}} from payload a5 62 49 44 64 44 32 42 31 62 4d 31 fa 40 89 1d dc 62 4d 32 fa 40 90 d4 b0 63 4d 31 30 fa 40 90 d4 b0 64 54 45 4d 50 fa 41 a3 00 00 using CBOR

## 4.7 ABCL data format

With AllThingsTalk Binary Conversion Language ​(ABCL) only the data bytes are send and the payload needs to be parsed by AlthingsTalk server.

Click on settings (as instructed on chapter 4.5)

Now select from the drop down menu “ payload formats”

>>>>>>>>>>>>>>>>>>>>>>>>>>

In the screen that appears copy/paste the following :

  {
  "sense": [
    {
      "asset": "ID",
      "value": {
        "byte": 0,
        "bytelength": 4,
        "type": "string"
      }
    },
    {
      "asset": "M1",
      "value": {
        "byte": 4,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    },
    {
      "asset": "M2",
      "value": {
        "byte": 8,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    },
    {
      "asset": "M10",
      "value": {
        "byte": 12,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    } ,
    {
      "asset": "TEMP",
      "value": {
        "byte": 16,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    }
  ]
}

Press “save” and you are done.

If you finished press DEBUG to see the packages coming in, once the board starts sending.

With ABCL it should look like:

Binary Conversion	2020-09-06T12:39:19	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 0.6958012580871582}, "M2": {"value": 1.1277278661727905}, "M10": {"value": 1.5160558223724365}, "TEMP": {"value": 21.4375}} from payload 44 32 42 31 3f 32 20 08 3f 90 59 63 3f c2 0e 1e 41 ab 80 00 using ABCL

# 5. Configure T-Mobile

## 5.1 Configure T-Mobile

### 5.1.1 Login
https://portal.iotcreators.com/auth/login

Sign in or sign up.

### 5.1.2 Register device FIRST

BEFORE DOING ANYTHING ELSE MAKE SURE TO REGISTER THE DEVICE

Sign up to a plan / project if you have not done so:

If you have a project , double on that and now register you device with the IMEI

After signing up you should see the device showing up in the device overview of the project.

### 5.1.3 Forwarding data to AllThingsTalk
Actually the T-Mobile portal is only storing and forwarding the data to a place for further processing. Here we use the forward to AllThingsTalk. To setup the forwarding link see : https://docs.iotcreators.com/docs/integration-with-allthingstalk
The most important part is to have your screen look like this :
## 5.2 AllThingsTalk login

https://maker.allthingstalk.com/signin

Sign in or sign up.

NOTE : This is a DIFFERENT URL than for Vodafone. Completely different environment and as such the login credentials and password are unique for this environment (and thus different to Vodafone)
### 5.2.1 Create a new ground

The back-end is organized in so-called “grounds”. A ground is a group of devices. For this
document I will call it “sps30”. Then double click on “sps30” and you will see the following:

### 5.2.2 Create a new device

Click on “+NEW DEVICE”, and you will get something like. >>>>>>>>>>>>>>>>>>>>>>>

I select “your own NB-IoT device” and you can select T-mobile: vvvvvvvvv

The following information is requested :

Enter a name >>>
( e.g. SPS30+DS18)

Printed on the card >>>

Optional >>>>

Optional >>>

Last press >>>>>>>>>

IMEI can be obtained from the sim card : AT+CGSN (already printed on the card)
IMSI can be obtained from the sim card : AT+CIMI
SIM can be obtained from the sim card : AT+CCID (already printed on the card)

### 5.2.3 Create assets

Now create new asset, press “+NEW ASSET”

For Example4 you need to add the following information:

name Choose type	CREATE ASSET
ID	String	x
M1	Number	x
M2	Number	x
M10	Number	x
TEMP	Number	x

- Each asset needs to be created separate.
- Use capitals for the name as shown.
- If you change or add in the Example4, make sure to change/add here as well.

### 5.2.4 Jason or CBOR data format

You are done !

If you finished press DEBUG to see the packages coming in, once the board starts sending

JUST BE AWARE IT CAN TAKE UP TO 10 MINUTES AFTER THE DATA IS SHOWING UP IN T-MOBILE DEVICE OVERVIEW IS SHOWING UP IN ALLTHINGSTALK

Jason will look like:

Binary Conversion	2020-09-06T12:50:02	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 2.86}, "M2": {"value": 3.02}, "M10": {"value": 3.02}, "TEMP": {"value": 20.31}} using JSON

CBOR will look like:

Binary Conversion	2020-09-06T12:57:23	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 4.284894943237305}, "M2": {"value": 4.525962829589844}, "M10": {"value": 4.525962829589844}, "TEMP": {"value": 20.375}} from payload a5 62 49 44 64 44 32 42 31 62 4d 31 fa 40 89 1d dc 62 4d 32 fa 40 90 d4 b0 63 4d 31 30 fa 40 90 d4 b0 64 54 45 4d 50 fa 41 a3 00 00 using CBOR

### 5.2.5 ABCL data format

With AllThingsTalk Binary Conversion Language ​(ABCL) only the data bytes are send and the payload needs to be parsed by AlthingsTalk server.

Click on settings:

Now select from the drop down menu “ payload formats”

>>>>>>>>>>>>>>>>>>>>>>>>>>

In the screen that appears copy/paste the following :

  {
  "sense": [
    {
      "asset": "ID",
      "value": {
        "byte": 0,
        "bytelength": 4,
        "type": "string"
      }
    },
    {
      "asset": "M1",
      "value": {
        "byte": 4,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    },
    {
      "asset": "M2",
      "value": {
        "byte": 8,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    },
    {
      "asset": "M10",
      "value": {
        "byte": 12,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    } ,
    {
      "asset": "TEMP",
      "value": {
        "byte": 16,
        "bytelength": 4,
        "signed": false,
        "byteorder": "little",
        "type": "number"
      }
    }
  ]
}

Press “save” and you are done.

If you finished press DEBUG to see the packages coming in, once the board starts sending.

JUST BE AWARE IT CAN TAKE UP TO 10 MINUTES AFTER THE DATA IS SHOWING UP IN T-MOBILE DEVICE OVERVIEW IS SHOWING UP IN ALLTHINGSTALK

With ABCL it should look like:

Binary Conversion	2020-09-06T12:39:19	INFO	Parsed {"ID": {"value": "D2B1"}, "M1": {"value": 0.6958012580871582}, "M2": {"value": 1.1277278661727905}, "M10": {"value": 1.5160558223724365}, "TEMP": {"value": 21.4375}} from payload 44 32 42 31 3f 32 20 08 3f 90 59 63 3f c2 0e 1e 41 ab 80 00 using ABCL

# 6 Usage
## 6.1 Sketch usage
### 6.1.1 LED

The led on the board can show the following :

During start-up :
GREEN : Detecting DS18x20.
YELLOW : Detected DS18x20 now detecting SPS30.
BLUE : Detected SPS30 now initializing SARA and connecting with provider.
OFF	: Start-up complete

Normal working
Led is flashing MAGENTA after every 5 readings for the MEASUREINTERVAL (still-alive-signal)
Led is flashing GREEN when sending data. (very short)
Led is flashing RED, sending failed retry is planned.

Error
Led is blinking on and off RED (1 second frequency), something went wrong. On hold !

### 6.1.2 No Debug selected

After compiling and uploading you do NOT have to connect a terminal. If you do however, you will see progress messages and measurement information from the SPS30. Be reminded that you can connect a terminal later on if you want, set to 115200, and it will show SPS30 measured information.

### 6.1.3 Debug selected

If either SKETCH_DEBUG, SPS30_DEBUG or SODAQ_DEBUG is selected, you must connect a terminal. The sketch will wait for you to press <enter> before start-up. It will show, next to the normal progress messages and measurement information from the SPS30, debug information about the selected area(s). Once you are done, you must disable the debug in the source code and recompile.

### 6.1.4 Idle mode

While the SPS30 is planned to > 8 year lifetime, if the interval between measurements is larger than 60 seconds the SPS30 will be put idle. The ventilator will stop spinning and no measurements are performed. The interval time is reduced with 10 seconds, as a 10 second delay will be applied after the SPS30 is started when the interval time expires.
## 6.2 AllThingsTalk

### 6.2.1 DEBUG
If you are in DEBUG view, you should see regular (depending on the settings in chapter 3.3) the following information :

Binary Conversion	2020-04-03T18:35:45	INFO	Parsed {"ID": {"value": "1A76"}, "M1": {"value": 3.02}, "M2": {"value": 3.34}, "M10": {"value": 3.57}, "TEMP": {"value": 23.47}} using JSON

If you only hex-decimal numbers… something is wrong in the formatting of the data that is sent.

### 6.2.3 CHARTS or LIVE

Selecting LIVE you will get the information received over the past minutes, where CHARTS can provide the information received over a longer period.

Select in the top the values you want to monitor. In the example below that is humidity, M10, M2 and M1