Using Sparkfun library UBLOX GPS library for SODAQ

# Background

The SODAQ board contains a SAM-M8Q Ublox GNSS / GPS receiver. This receiver is very comprehensive and can be configured to your needs, but has limited examples from SODAQ.

Sparkfun (www.sparkfun.com) is a supplier of many different boards and sensors, which it supports with many (great) libraries. They also have boards with Ublox GNSS / GPS receiver, including the SAM-M8Q (https://www.sparkfun.com/products/15210).

Their library (https://github.com/sparkfun/SparkFun_Ublox_Arduino_Library) is very complete and can be used with minor adjustment for the SODAQ board.

This document describes the must-do change and optional changes.

1 May 2020 / version 1.0

Paul van Haastrecht
paulvha@hotmail.com

# 1. (MUST DO) Hardware enablement

If you use the Sparkfun library as-is you will get an error:
Ublox GPS not detected at default I2C address. Please check wiring. Freezing.

Unlike the Sparkfun boards, the SAM-M8Q needs to be “turned-on” on the SODAQ board. Turning-on is applying power and the SAM-M8Q needs time to start and stabilize. The 2000mS delay gave stable performance.

## 1.1 Change to library
The following code needs to be added in Sparkfun_Ublox_Arduino_library.cpp with the call
begin(TwoWire &wirePort, uint8_t deviceAddress).

Add the following :

// special for SODAQ to enable GPS module
#if defined(ARDUINO_SODAQ_AUTONOMO) || defined(ARDUINO_SODAQ_SARA) || defined(ARDUINO_SODAQ_SFF)
  pinMode(GPS_ENABLE, OUTPUT);
  digitalWrite(GPS_ENABLE, HIGH);
  delay(2000);
#endif

After changing the call should look like : (removed comment lines)

boolean SFE_UBLOX_GPS::begin(TwoWire &wirePort, uint8_t deviceAddress)
{
  commType = COMM_TYPE_I2C;
  _i2cPort = &wirePort; //Grab which port the user wants us to use
   _gpsI2Caddress = deviceAddress; //Store the I2C address from user

// special for SODAQ to enable GPS module
#if defined(ARDUINO_SODAQ_AUTONOMO) || defined(ARDUINO_SODAQ_SARA) || defined(ARDUINO_SODAQ_SFF)
  pinMode(GPS_ENABLE, OUTPUT);
  digitalWrite(GPS_ENABLE, HIGH);
  delay(2000);
#endif

  return (isConnected());
}

## 1.2 OR Change to sketch

Instead of changing Sparkfun_Ublox_Arduino_library.cpp a change in the sketch setup() can also be applied before a call :
if (myGPS.begin() == false) {}

Add there :

  pinMode(GPS_ENABLE, OUTPUT);
  digitalWrite(GPS_ENABLE, HIGH);
  delay(2000);

# 2. (Optional) checkUblox errors

Some examples (like Example 1_BasicNMEARead), would not compile due to :
error: no matching function for call to 'SFE_UBLOX_GPS::checkUblox()'

It looks that the checkUblox() has been changed after the examples were created. The quickest way to solve is to define an ubxPacket-object and add a pointer to that in the call. It does not need to be initialized, as it is not used in I2C communication.

ubxPacket pp;
myGPS.checkUblox(&pp);

# 3. (Optional) NMEA messages not showing
After running example3_GetPosition, the examples with NMEA would not work without removing and reconnecting the power

The root cause is because the NMEA messages were disabled in example3_GetPosition with :

myGPS.setI2COutput(COM_TYPE_UBX); //Set the I2C port to output UBX only (turn off NMEA noise)

Instead of removing the power, this can also be resolved by adding at the end of setup() in example3

myGPS.setI2COutput(COM_TYPE_NMEA); //Set the I2C port to output NMEA only

# 4. (INFO) save configuration

A line like : myGPS.saveConfiguration(); //Save the current settings to flash and BBR has limited impact on the SODAQ board,
as the backup-power is the same as the VCC. So removing the power from the SODAQ board removes the backup power and thus clears the BackupPowerRAM (BBR). Some of the Sparkfun boards have a battery connected to the backup power. If there is a battery, this approach would will help to find the different satellites faster (warm boot, instead of cold boot ).

The impact for the SODAQ board is that changes applied will be lost after power off. E.g. setting a new I2C address will work, but will be reverted back to the original (0x42) a number of example sketch and satellite information is lost.
# 5. (Optional) getting firmware information

The Sparkfun library has an example8_GetProtocalVersion() to display the protocol version of the SAM-8MQ. However if you want to the firmware information, like which is displayed at reboot. The following approach can display the following information:

ROM CORE 3.01 (107888)
00080000 FWVER=SPG 3.01
PROTVER=18.00
GPS;GLO;GAL;BDS
SBAS;IMES;QZSS

Changes are needed on the following places :
1. Within an example sketch
2. Sparkfun_Ublox_Arduino_library.h
3. Sparkfun_Ublox_Arduino_library.cpp
## 5.1 Changes to an example sketch

### 5.1.1 Add the following routine :

void get_firmware()
{
  uint8_t len, buff_len = 250;
  uint8_t buff[buff_len];

  if (myGPS.getFirmware(buff, buff_len, &len)) {

    Serial.print(F("Version information:"));

     for (int location = 0; location < len; location++)
     {
       if (location % 30 == 0) Serial.println();
       Serial.write(buff[location]);
     }
     Serial.println();
  }
}

### 5.1.2 Add at the end of setup :

get_firmware();

## 5.2 Sparkfun_Ublox_Arduino_library.h

Add in the public area (around line 455):
    boolean getFirmware(uint8_t *buf, uint8_t len, uint8_t *r_len, uint16_t maxWait = defaultMaxWait); // added PVH

## 5.3 Sparkfun_Ublox_Arduino_library.cpp

boolean SFE_UBLOX_GPS::getFirmware(uint8_t *buf, uint8_t len, uint8_t *r_len,uint16_t maxWait)
{
  uint8_t location;

  //Send packet with only CLS and ID, length of zero. This will cause the module to respond with the contents of that CLS/ID.
  packetCfg.cls = UBX_CLASS_MON;
  packetCfg.id = UBX_MON_VER;

  packetCfg.len = 0;
  packetCfg.startingSpot = 0;

  if (sendCommand(&packetCfg, maxWait) != SFE_UBLOX_STATUS_DATA_RECEIVED) // We are only expecting data (no ACK)
    return (false); //If command send fails then bail

  //Payload should now contain ~220 characters (depends on module type)
  for (location = 0; location < packetCfg.len ; location++)
  {
      buf[location] = payloadCfg[location];
      if (location + 1 > len) break;
  }

  buf[location] = 0x0; //terminate
  *r_len = location;

  return (true); //Success!
}